## Slide 1: BOOLEAN ALGEBRA

## Slide 2: INTRODUCTION
Developed by English Mathematician George Boole in between 1815 - 1864.
It is described as an algebra of logic or an algebra of two values i.e True or False.
The term logic means a statement having binary decisions i.e True/Yes or False/No.

## Slide 3: APPLICATION OF BOOLEAN ALGEBRA

## Slide 4: APPLICATION OF BOOLEAN ALGEBRA
It is used to perform the logical operations in digital computer.
In digital computer True represent by ‘1’ (high volt) and False represent by ‘0’ (low volt)
Logical operations are performed by logical operators. The fundamental logical operators are:
1. AND (conjunction)
2. OR (disjunction)
3. NOT (negation/complement)

## Slide 5: AND operator
It performs logical multiplication and denoted by (.) dot.
X Y X.Y
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 6: OR operator
It performs logical addition and denoted by (+) plus.
X Y X+Y
0 0 0
0 1 1
1 0 1
1 1 1

## Slide 7: NOT operator
It performs logical negation and denoted by (-) bar. It operates on single variable.
X X (means complement of x)
0 1
1 0

## Slide 8: Truth Table
Truth table is a table that contains all possible values of logical variables/statements in a Boolean expression.
No. of possible combination =
2n, where n=number of variables used in a Boolean expression.

## Slide 9: Truth Table
The truth table for XY + Z is as follows:
Dec X Y Z XY XY+Z
0 0 0 0 0 0
1 0 0 1 0 1
2 0 1 0 0 0
3 0 1 1 0 1
4 1 0 0 0 0
5 1 0 1 0 1
6 1 1 0 1 1
7 1 1 1 1 1

## Slide 10: Tautology & Fallacy
If the output of Boolean expression is always True or 1 is called Tautology.
If the output of Boolean expression is always False or 0 is called Fallacy.

## Slide 11: Tautology & Fallacy

## Slide 12: Exercise
1. Evaluate the following Boolean expression using Truth Table.
(a) X’Y’+X’Y (b) X’YZ’+XY’
(c) XY’(Z+YZ’)+Z’
2. Verify that P+(PQ)’ is a Tautology.
3. Verify that (X+Y)’=X’Y’

## Slide 13: Implementation
Boolean Algebra applied in computers electronic circuits. These circuits perform Boolean operations and these are called logic circuits or logic gates.

## Slide 14: Logic Gate

## Slide 15: Logic Gate
A gate is an digital circuit which operates on one or more signals and produce single output.
Gates are digital circuits because the input and output signals are denoted by either 1(high voltage) or 0(low voltage).
There are three basic gates and are:
1. AND gate
2. OR gate
3. NOT gate

## Slide 16: AND gate

## Slide 17: AND gate
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high.
AND gate takes two or more input signals and produce only one output signal.
Input A | Input B | Output AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 18: OR gate

## Slide 19: OR gate
The OR gate is an electronic circuit that gives a high output (1) if one or more of its inputs are high.
OR gate also takes two or more input signals and produce only one output signal.
Input A | Input B | Output A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 20: NOT gate

## Slide 21: NOT gate
The NOT gate is an electronic circuit that gives a high output (1) if its input is low .
NOT gate takes only one input signal and produce only one output signal.
The output of NOT gate is complement of its input.
It is also called inverter.
Input A | Output A
0 | 1
1 | 0

## Slide 22
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 23
AND Gate
So while going out of the house you set the "Alarm Switch" and if the burglar enters he will set the "Person switch", and tada the alarm will ring.
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 24
AND Gate
PRACTICAL APPLICATIONS OF LOGIC GATES
Electronic door will only open if it detects a person and the switch is set to unlocked.
Microwave will only start if the start button is pressed and the door close switch is closed.

## Slide 25
OR Gate
You would of course want your doorbell to ring when someone presses either the front door switch or the back door switch..(nice)
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 26
NOT Gate
When the temperature falls below 20c the Not gate will set on the central heating system (cool huh).
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 27
NAND, NOR XOR, XNOR GATES

## Slide 28
NAND Gate
Known as a “universal” gate because ANY digital circuit can be implemented with NAND gates alone.

## Slide 29
NAND Gate
NAND
X
Y
Z
X Y Z
0 0 1
0 1 1
1 0 1
1 1 0
Z = ~(X & Y)
nand(Z,X,Y)

## Slide 30
NAND Gate
X
X
F = (X•X)’
= X’+X’
= X’
X
Y
Y
F = ((X•Y)’)’
= (X’+Y’)’
= X’’•Y’’
= X•Y
F = (X’•Y’)’
= X’’+Y’’
= X+Y
X
X
F = X’
X
Y
Y
F X•Y
F = X+Y

## Slide 31
NOR Gate

## Slide 32
NOR Gate
NOR
X
Y
Z
X Y Z
0 0 1
0 1 0
1 0 0
1 1 0
Z = ~(X | Y)
nor(Z,X,Y)

## Slide 33
Exclusive-OR Gate

## Slide 34
Exclusive-OR Gate
X Y Z
XOR
X
Y
Z
0 0 0
0 1 1
1 0 1
1 1 0
Z = X ^ Y
xor(Z,X,Y)

## Slide 35
Exclusive-NOR Gate
X Y Z
XNOR
X
Y
Z
0 0 1
0 1 0
1 0 0
1 1 1
Z = ~(X ^ Y)
Z = X ~^ Y
xnor(Z,X,Y)

## Slide 36
POWER CONSUMPTION OF SYSTEM

## Slide 37: Basic Theorem of Boolean Algebra
T1 : Properties of 0
  (a) 0 + A = A (b) 0 A = 0
T2 : Properties of 1
  (a) 1 + A = 1 (b) 1 A = A

## Slide 38: Basic Theorem of Boolean Algebra
T3 : Commutative Law
  (a) A + B = B + A (b) A B = B A
T4 : Associate Law
  (a) (A + B) + C = A + (B + C) (b) (A B) C = A (B C)
T5 : Distributive Law
  (a) A (B + C) = A B + A C (b) A + (B C) = (A + B) (A + C)
  (c) A+A’B = A+B

## Slide 39: Basic Theorem of Boolean Algebra
T6 : Indempotence (Identity ) Law
  (a) A + A = A (b) A A = A
T7 : Absorption (Redundance) Law
  (a) A + A B = A (b) A (A + B) = A

## Slide 40: Basic Theorem of Boolean Algebra
T8 : Complementary Law
  (a) X+X’=1
  (b) X.X’=0
T9 : Involution
  (a) x’’ = x
T10 : De Morgan's Theorem
  (a) (X+Y)’=X’.Y’
  (b) (X.Y)’=X’+Y’

## Slide 41: De Morgan's Theorem

## Slide 42: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 43: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 44: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 45: De Morgan's Theorem 2
Theorem 1 A + B = A . B

## Slide 46: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 47: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 48: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 49: Thank You